## Slide 1: HP ProLiant ML110 G5 Server
12 November 2007 Announcement
HP Industry Standard Servers
Notes: © Copyright 1996, 1997–2007 Hewlett-Packard Development Company, L.P.
The information contained in this presentation is proprietary to Hewlett-Packard Company and is offered in confidence, subject to the terms and conditions of a Confidential Disclosure Agreement (CDA).
HP requires customers and partners to have signed a CDA in order to view this training. The information contained in this training is HP Confidential, but will become HP Restricted after announcement.
HP does not warrant or represent that it will introduce any product to which the information relates. The information contained herein is subject to change without notice. HP makes no warranties regarding the accuracy of this information. The only warranties for HP products and services are set forth in the express warranty statements accompanying such products and services. Nothing herein should be construed as constituting an additional warranty. HP shall not be liable for technical or editorial errors or omissions contained herein.
This is an HP copyrighted work that may not be reproduced without the written permission of HP. You may not use these materials to deliver training to any person outside of your organization without the written permission of HP.
Microsoft and Windows are U.S. registered trademarks of Microsoft Corporation.
Intel and Pentium are trademarks or registered trademarks of Intel Corporation in the U.S. and other countries.
New Product Introduction HP Restricted

## Slide 2: What is announcing
HP ProLiant ML110 G5
Announcing generation 5 of ML110
Key new G5 features or capabilities
Performance: Quad-Core Intel® Xeon® processors 3200 series (Intel Kentsfield) Memory: Up to 8GB PC2-6400 unbuffered DDR2 ECC 800MHz I/O: (4) total I/O slots: (1) 3.3V PCI and (3) PCI-Express (1 x8 & 2X1) Storage controller: Integrated SATA controller Networking: Embedded NIC 5722 Management: Lights Out 100c Remote Management Card (Optional)
Availability: 12 November 2007
ML110 G5 on HP.com
ProLiant Site Index: http://h18000.www1.hp.com/products/servers/siteindex.html
CD-ROM Drive
Power LED
Drive Activity LED
Well ventilated chassis design
SAS Cable
HDD controller card (Optional)
Main System Board
HP LO 100c Management Card (Optional)
Rear System Fan
365W Power Supply
5
6
7
8
9
10
1
2
3
4
Notes: What is announcing
    The HP ProLiant ML110 G5 (ML110 G5) is an Intel-based, single processor, entry-level, 4U form factor tower server supporting the following Intel processors:
      Quad-Core Intel® Xeon® processors 3000 and 3200 sequence
      Dual-Core Intel® Core 2 processors 4000 sequence
      Dual-Core Intel® Pentium® processors 2000 sequence
      Single-Core Intel® Celeron® processors 400 Sequence
  What’s new
    On the day of announcement, HP will announce these new features and functionality:
      New Quad-Core Intel® Xeon® processors 3200 series (Intel Kentsfield)
      512MB standard / 8GB maximum of PC6400 DDR2, unbuffered ECC memory (1GB standard on SAS models)
      Six (6) port SATA storage controller with Embedded RAID, 0,1,1+0 on motherboard and HP 4 Internal Port SAS HBA with RAID SC40Ge
      Four (4) hard disk drive support: 3TB SATA maximum storage (utilizing 750GB CTO hard disk drive) and 1.2TB SAS maximum storage (4 x 300GB)
      Expansion slots:
        Slot 1: 32-bit/33MHz PCI at 3.3V slot
        Slot 2, 3: PCI-Express x8 connector with x1 link
        Slot 4: PCI-Express X8 connector with x8 link
      Embedded network interface card, NIC 5722
      Standard Lights Out 100 IPMI 2.0 reporting and optional Lights Out 100c Remote Management Card to decrease server/company downtime and increase productivity
  Warranty
    Hardware diagnostic support and repair is available for one year from date of purchase. Support for software and initial setup is available for 90 days from date of purchase. SATA hard drives have a one year warranty.

## Slide 3: Product and technology overview
Servers provide data to users on a network and designed for specific markets, needs, and applications
  Data, printers, and modems are shared
  Applications, such as email, are shared
  Internet connectivity is shared
  Network security is important
  Large amounts of data must be stored and processed
  The system must operate 24 hours a day, 7 days a week
ML110 G5 server
  Dependable, easy-to-use workgroup server for hosting basic file/print for 20 or fewer clients
  Platform for light application hosting, shared web access, groupware, or small database applications
  Entry-level for small businesses
  Same price as misapplied desktop PCs
Notes: <header>
<date/time>
Product and technology overview
    Servers provide data to users on a network. Servers are designed for specific markets, needs, and applications. They can be used where:
      Data, printers, modems, applications and Internet connectivity are shared
      Network security is important
      Large amounts of data must be stored and processed
      The system must operate 24 hours a day, 7 days a week
    Servers can be differentiated from desktop computers based on hardware and technology:
      Processors — Servers support multiple processors, whereas desktop computers support only one processor.
      Memory — Servers support significantly larger amounts of memory than desktop computers.
      Storage — Servers are designed for more external and internal storage. Desktop computers are not designed for large amounts of either type of storage.
      System architecture — Servers are designed to minimize bottlenecks that can be encountered when multiple users access a server simultaneously.
      Video and sound — Desktop computers typically contain more advanced video and sound technologies than servers because they are more often used for running and viewing graphic-intensive games and programs.
  Why this product now?
    The ML110 G5 incorporates features for small / medium businesses and remote site locations:
      The focus on design provides a simplified server with the right features limiting the price of the server to the small business. By not including expensive graphics or sound cards found in desktop PCs the ML110 G5 is able to offer true server functionality at an equivalent desktop PC price.
      The ProLiant 100 Series servers have tailored features to reflect the usage needs of small businesses and branch offices. The ML110 G5 incorporates features for small / medium businesses and remote site locations.

## Slide 4: New capability − latest Intel® Xeon® 3000 sequence processors
Quad-Core Intel® Xeon® processors 3200 series
  For one-way servers
  Significant performance headroom for multi-threaded applications
  Helps boost system utilization through virtualization and application responsiveness
Thermal Design Power
  Significantly lower power helps improve data center density and power/thermal operating costs
Flexibility for 64-bit and 32-bit applications and operating systems
  Allows both 32-bit and 64-bit applications to run
8MB+ shared L2 cache
  Increases efficiency of L2 cache-to-processor data transfers, maximizing main memory to processor bandwidth and reducing latency
Faster 1066MHz system bus
  Provides increased throughput
Notes: New capability − latest Intel® Xeon® processors
    Intel processor series numbers help differentiate processor features beyond front-side bus speed and brand name. Intel offers four processor number sequences for server applications:
      Intel® Xeon® processor 3000 sequence (Dual-Core Intel® Xeon® processor 3000 series and Quad-Core Intel® Xeon® processor 3200 series) — For economical, dependable, general-purpose one-way servers well-suited for small business, the basic enterprise server needs, and low-cost High Performance Computing.
      Intel® Xeon® processor 5000 sequence — For volume, energy-efficient, general purpose, and cost-effective two-processor systems and enterprise infrastructure applications.
      Intel® Xeon® processor 7000 sequence — For four-processor to 32-processor systems, ultra-dense deployments, and data- and transaction-intensive applications.
      Intel® Itanium® 2 processor 9000 sequence — Maximum RISC-based performance and scalability for critical business computing needs, including database applications, data warehousing, large-scale ERP and business analytics.
  New processor features
    Intel® Xeon processor 3200 series entry-level server platforms integrate advanced technologies:
      Quad-core, 64-bit computing based on the Quad-Core Intel® Xeon® processors 3200 series for one-way servers.
      Thermal Design Power reduces operating costs while delivering higher performance. Lower consumption can also result in slower fans and quieter servers.
      Flexibility for 64-bit and 32-bit applications and operating systems allows both 32-bit and 64-bit applications to run.
      8MB+ shared L2 cache increases efficiency of L2 cache-to-processor data transfers, maximizing main memory to processor bandwidth and reducing latency.
      Faster 1066 MHz system bus for increased throughput.
      High-speed DDR2 memory with up to 8GB of memory keeps more data closer to the processor and helps eliminate slowdowns from memory bottlenecks.

## Slide 5: New capability − Lights-Out 100 Remote Management Card
HP ProLiant ML110 G4 Lights-Out 100c Remote Management Card
  Optional 445513-B21
  Basic, affordable remote management for ProLiant 100 series
  OS independent server troubleshooting and recovery
    Remotely control system console and power
    View system environment health and system event log
  Software and firmware update
    Remotely control attached USB storage
  Operating system administration
    Remotely control system console
Benefits:
  Reduce support cost and time
    Save time and money supporting network with full remote control of ProLiant 100 Series servers anytime, anywhere
  Easy ownership
    Essential remote management choices at affordable prices and easy to upgrade
  Asset protection
    Standards based security restricts access and encrypts data
  Maximize the reliability of investment
    Remote control when needed to keep business up and running
Notes: New capability − Lights-Out 100 Remote Management Card
    There is a new product specific option for the ML110 G5. It is the following:
      Lights-Out 100 Remote Management Card
    Lights Out LO100c is a family of Remote Management Cards for ProLiant 100 series servers that do not have embedded LO100i. The LO100c allows customers, or their service providers, to remotely manage ProLiant servers over a LAN or the Internet from anywhere, anytime regardless whether the server is located in the same building, across town, or around the globe. HP LO100c provides virtual media and Virtual KVM for full remote graphical console capabilities in entry-level servers. It also enables anytime access to system management information such as hardware health and event logs. These remote control capabilities dramatically reduce the need to physically visit or find onsite assistance to support ProLiant 100 Series servers for troubleshooting, deployment and updating.
  What’s new
    The new HP PL100 G5 LO100c Kit is now available for ProLiant 100 G5 series servers that require a management card rather than advanced licenses. This card does not work on previous generation tower servers which still have their separate, specific LO100c Remote Management Cards.
      Supports ProLiant ML110 G5 server
      Improvements to virtual media with the addition of USB 2.0 and DVD-ROM support plus simplified virtual media (floppy and CD with no FTTP server requirements)
      Enhanced browser interface and embedded Virtual KVM provides OS-independent remote graphical console
      Easy to implement, standards based, Secure Socket Layer (SSL) and Secure Shell (SSH), restricts access and encrypts data.
      Data encryption of browser and command line interfaces provides security to assets, data, and information.
    For more information, go to the Lights Out LO 100C home page on HP.com: http://h18013.www1.hp.com/products/servers/management/remotemgmt/lightsout100/index.html?jumpid=reg_R1002_USEN#models.

## Slide 6: ML110 G4 compared to ML110 G5
 | ML110 G4 | ML110 G5
Processor | Intel® Xeon® 3000 Series, Pentium® D, and Celeron® D Processors - Processor speed up to 2.4 GHz - FSB up to 1066MHz - Dual Core Supported | Intel® Xeon® 3000 Series, Pentium® D, and Celeron® D Processors - Processor speed up to 2.66GHz - FSB up to 1333MHz - Dual, Quad Core Supported
Memory | DDR2 PC5300 SDRAM (8GB maximum/512 standard ECC memory | DDR2 PC6400 SDRAM (8GB maximum/512 standard), unbuffered ECC memory
Storage | Four (4) hard disk drives standard on MB(Embedded BIOS RAID 0,1,1+0) | Four (4) hard disk drives standard on MB controller (Embedded BIOS RAID 0,1,1+0)
Management | Lights-Out 100c Remote Management Card (Optional)-Video Memory: 2MB | Lights-Out 100 Remote Management Card (Optional) Video memory: 8MB
I/O | 4 Total: 2 PCI-Express (x4 and x8) 2 3.3 V PCI | 4 Total: 3 PCI-Express (1x8 and 2x1) 1 3.3 V PCI
Notes: ML110 G4 compared to ML110 G5
    This slide shows the differences between the features of the ML10 G4 and the ML110 G5.

## Slide 7: ProLiant 100 series
Performance/features
Price
Cost-conscious
Aggressive price points
Industry standard hardware
Small business
1-50 clients (typically 10)
File and print, web access
Value conscious
Sophisticated small-business
1-99 clients
Value reliability, ease of use, headroom
Dedicated IT resource
Value conscious
Med/large corporate workgroups
500+ clients
Remote locations
Infrastructure, database, e-commerce
Performance, expansion,
Manageability, availability and stability
ML100 Series
ML300 Series
Simple, affordable 1/2P
Enterprise class 1/2P
Notes: <header>
<date/time>
ProLiant 100 series
    The HP ProLiant ML/DL 100 series is the entry-level of the ProLiant server line designed to deliver appropriate technology to specific market segments. The 100 series will offer a limited suite of options and leverage the various operating system enabled manageability features. The ProLiant 100 series is optimized for small / medium businesses running small business applications and enterprises running high performance technical computing solutions. These clients usually have 1-50 clients (usually peer-to-peer), and use file and print and web access (modem) servers. The ideal customer for the HP ProLiant ML/DL 100 series works in single homogeneous environments with little or no IT staff and values the low cost that the HP ProLiant 100 series provides.
    The HP ProLiant ML/DL 300 series are enterprise class servers providing industry-leading reliability, features and advanced manageability tools. The HP ProLiant 300 series are targeted towards a more IT sophisticated small / medium business.
    The HP ProLiant 300 series are targeted towards a more IT sophisticated small / medium businesses and enterprise companies with as many as 500+ clients. Many of the features the ProLant 300 series delivers to the enterprise class, both single and dual processor systems, are not required by the simple, affordable small and medium business segment.
  Competitive price point
    The HP ProLiant 100 server series leverages the priorities on which ProLiant was built, reliability and performance, and has specifically targeted these servers to incorporate features for the targeted customer usage such as small / medium businesses and high performance computing. Focus on design provides a much more simplified server with the right features, limiting the cost burdened to the server and qualification process. The new 100 server series designs have tailored features that closely reflect their usage needs and the addition of qualified third-party configuration vendors to enable a simpler, more affordable solution.

## Slide 8: Why the ProLiant 100 series?
Features
Appropriate, competitive, industry standard
Features defined by competition (Dell, IBM, whiteboxes)
TCE
Provide positive customer experience through ease of doing business, reliable products, capitalizing on HP portfolio and presence, and HP World Class Support
Price
100 Series products must be priced competitively (parity to Dell and IBM)
(meet competition)
(beat competition)
(meet competition)
Win customers in simple, affordable segment
Objective
#1
value =
features + TCE
price
Tactics
deliver more value
than competitors
Notes: <header>
<date/time>
Why the ProLiant 100 series
    HP continues to deliver the best value to our customers to continue to win competitive bids. A basic definition of value, as perceived by HP customers, is (features + experience)/price. Value points change depending upon target segment:
      For the enterprise class, single and dual processor systems, the 300 series delivers segment winning value by offering the best features and total customer experience (TCE) of all server vendors.
      For the simple, affordable space, the single most important variable factor is price.
    Focusing on the specific requirements of this space, the 100 series will offer appropriate functionality at competitive price points. The 100 series value proposition compared to HP competitors is TCE. These include:
      Ease of doing business
      Financing options
      HP portfolio of technology products
      HP partnership with technology providers (Microsoft, Oracle, etc)
      HP service and support
      HP standard for product quality

## Slide 9: Customer opportunities Look for these customers
  Well-suited and best value for:
    Small business owners and buyers looking for ways to grow business and manage operations more effectively and efficiently
    Basic enterprise, general purpose, or entry-level applications
    Low-cost High Performance Computing applications, personal cluster solutions, or work-group clusters
  Utilizing one-way ProLiant servers
  Supporting locations with a limited IT staff
  Obtaining data protection at an affordable price
  Relying on the server to run industry-standard applications
  Purchasing an easy-to-own server
Technology strategies: Utilizing one-way ProLiant servers for general purpose or entry-level systems
Customer size: Small to medium, basic enterprise, remote staff
Business requirement: Obtaining easy-to-own data protection at an affordable price
Target markets: Small and medium, HPC
Business requirement: Relying on the server to run industry-standard applications
Notes: <header>
<date/time>
Customer opportunities
    For selling opportunities, look for customers with the following business challenges:
      Utilizing one-way ProLiant servers for general purpose or entry-level systems. Why?
        The ML110 G5 is designed with a balanced architecture to drive the adoption of quad-core technology to its line of single processor systems. The ML110 G5 targets customers with single-tier, simple architectures, homogeneous environments with single applications and workloads, and requires very little IT support.
      Supporting locations with a limited IT staff. Why?
        The ML110 G5 is well-purposed for small businesses or remote sites with minimal technology skills, limited, or no IT staff. These customers need a reliable server that requires little attention or maintenance and has the warranties and support of a branded-top tier vendor. The ML110 G5 can be upgraded with the cost-effective HP Lights-Out 100c Remote Management card for remote sites or second offices.
      Obtaining data protection at an affordable price. Why?
        This an efficiently sized server that is ideal for small offices, first networks and remote sites. It delivers true server reliability and functionality for the price of a typical desktop computer.
      Relying on the server to run industry-standard applications. Why?
        Ideal applications include file and print, web messaging, small vertical applications or databases, and shared Internet access and LAN infrastructure. Ideal ML110 G5 rely on servers to run day-to-day applications for their growing businesses and they require a server powerful enough to drive these applications.
      Purchasing an easy-to-own server. Why?
        Designed specifically for businesses that require an easy-to-configure, easy-to-use platform. All major components are designed to be removed or installed with little effort. When growth becomes necessary for a small business network, the ML110 G5 is easily reconfigurable.

## Slide 10: ML110 G5 front panel components
Description | 
Optical drive Optical drive manual eject hole Optical drive eject button Optical drive activity indicator Half-height common bay (ODD) Power button Power LED indicator | Drive activity indicator Front USB 2.0 ports Hard drive EMI shield screw Hard drive EMI shield Optical drive spare screws Hard drive spare screws
13
1
2
3
4
5
6
7
8
9
10
11
12
Notes: ML110 G5 front panel components
    This slide shows the front panel components on the ML110 G5.

## Slide 11: ML110 G5 rear panel components
Description | 
PSU fan Power supply outlet PS/2 mouse port PS/2 keyboard port VGA port Serial port Rear USB 2.0 ports LAN port (RJ-45) HP LO 100 Remote Management Card port | PCI slot covers Kensington lock notch Thumbscrew for access panel Rear system fan Cable lock provision tab PCI slot cover lock
15
14
13
12
11
1
2
3
4
5
6
7
8
9
10
Notes: ML110 G5 reart panel components
    This slide shows the rear panel components on the ML110 G5.

## Slide 12: ML110 G5 motherboard block diagram
Intel® Xeon 3000 MCH
DMI
x8 PCI-E slot
ICH9R
6xSATA
4 USB Ports (rear)
2 USB Ports (front)
2 USB Port (internal)
Un-buffered w/ ECC DDR2
(667/800)
Intel® Xeon 3000, 3100, 3200, 3300 Pentium D, Celeron D Series Processors
x1
VGA
GbE
x1
BCM5722
PCI 32bit 3.3V slot
ServerEngine
Pilot 2
Kbd/Ms
Full-Feature IPMI
Option Slot
USB
Serial
LPC Flash
SPI Flash ROM
1333/1066/800 FSB
x1 PCI-E
x1 PCI-E
Notes: ML110 G5 motherboard block diagram
    This slide shows the motherboard block diagram for the ML110 G5.

## Slide 13: Attach recommendations
Base model
  SATA Models
    ML110 G5 Pentium E2160 SATA - 444809-001
    ML110 G5 Xeon 3065 SATA - 444810-001
  SAS Models
    ML110 G5 XEON 3065 SAS - 444811-001
  Factory integrated
    ML110G5 CTO 445607-B21
What options are associated with this product or solution?
  Additional memory
  Processors
    Processor upgrades, available through CTO only
      Quad-Core Intel® Xeon® Processor X3220 (2.40GHz, 95W,1066 FSB,8M)
      Quad-Core Intel® Xeon ® Processor X3210 (2.13GHz, 95W,1066 FSB,8M)
Management
  HP ProLiant ML110 G5 Lights-Out 100 Remote Management Card
Storage
  Additional hard disk drives
Storage controller
  SAS Models
    HP SC40Ge Host Bus Adapter with RAID 0, 1, 1+0 support
Backup
  HP StorageWorks DAT 40, 72, or 160 USB Internal Tape Drive
  HP StorageWorks SCSI 40, 72, or 160 USB Internal Tape Drive
  HP D2D Backup System HP StorageWorks D2D110 Backup System ((1 or 2TB of Disk Storage)
Rack and power
  HP T750 or T1000 UPS
Notes: <header>
<date/time>
Attach recommendations
    This slide shows the suggested or recommended attach options for the ML110 G5. For part numbers and options details, see the ML110 G5 Quick Specs at http://h18004.www1.hp.com/products/quickspecs/12867_na/12867_na.html.
  Services
    Recommended Care Pack offerings include:
        Three-year, next business day onsite 9-hour x 5-day coverage, hardware support
        Hardware Installation
      Enhanced Care Pack offerings
        Three-year same business day onsite 13-hour x 5-day coverage, hardware support
        Hardware Installation plus operating system installation and startup
      Care Pack Services benefits
        Gain total control and maximum flexibility—resulting in tangible savings.
        Improve server availability with single-source support.
        Reduce the complexity of services and support resulting in productivity gains.
        Reduce deployment and manage ProLiant solutions smoothly and efficiently.
        Increase uptime and performance of your servers and solve applications problems quickly.
        Detect, diagnose and repair problems to quickly save time, money and resources.
    For more information, visit http://www.hp.com/services/proliantservices or http://www.hp.com/go/proliant/carepack.

## Slide 14: Competition
Dell - PowerEdge SC440
Dell - PowerEdge T105
IBM - System x3200
  Entry level, single processor servers
  Linux and Windows
  Targets small businesses, remote sites, general enterprise
  HP strengths
    Remote management
    Standard IPMI reporting
    Lights Out 100c Remote Management Card (Optional)
    Latest Quad-Core Intel® Xeon® processors 3200 series
    Better graphics memory
    10 USB ports
HP strategy against the competition
  High value for remote site or branch offices of small-medium size businesses
  Entry-level, single processor server solution for budget-conscious businesses
  Optional, industry standard remote manageability to manage remote locations
  HP service options to tailor support solutions
  Dependable performance
  Growth and adaptability are achieved through memory, hard disk drives, and PCI card
  Expandability gives provides future growth for small business
  True server at a desktop price
Source:
http://as.ideascp.com/cp/cp.aspx
Notes: <header>
<date/time>
Competition
    The main competitors to the ML110 G5 are:
      Dell - PowerEdge SC440
      Dell - PowerEdge T105
      IBM - System x3200
    All of these products are entry level, single processor servers running Linux and Windows, and target small businesses, remote sites, and general enterprise installations.
    HP strengths include:
      Remote management
      Standard IPMI reporting
      Lights Out 100c Remote Management Card (Optional)
      Latest Quad-Core Intel® Xeon® processors 3200 series
      Better graphics memory
      10 USB ports
    For a detailed competitive comparison between the ML110 G5 and these competing products, see the 12 November 1007 ML110 G5 Quick Reference Card.

## Slide 15: Product questions and answers
  Does the ML110 G5 support hot-plug hard disk drives?
  Does the ML110 G5 support Serial Attached SCSI (SAS) hard drives?
  Does the HP ProLiant ML110 G5 support embedded SATA RAID in a Windows configuration?
  Why do I need four memory slots?
  How does USB booting compare to floppy?
  What is PCI-Express and why is it important?
  Does the ML110 G5 support hot-plug hard disk drives?
  Does the ML110 G5 support Serial Attached SCSI (SAS) hard drives?
  Does the HP ProLiant ML110 G5 support embedded SATA RAID in a Windows configuration?
Notes: <header>
<date/time>
Product questions and answers
    Potential questions from customers may include:
      What is the general difference between the new ProLiant ML110 G5 and the old ML110 G4?
        ML110 G5 supports higher processor speed, up to 2.66 Ghz; supports higher Front Side Bus, up to 1333Mhz; supports Dual and Quad Core processors; supports DDR2 PC6400 SDRAM (8GB maximum / 512 standard), unbuffered ECC memory. Also, Lights-Out 100c Remote Management is improved from the previous generation, with 8Mb Video memory. ML110G5 also has four (4) I/O ports: 3 PCI-Express (1x8 and 2x1), 1 *3.3 V PCI.
      Why should I buy a ML110 G5 instead using a desktop PC as a server?
        ML110 G5 uses a chipset that is designed specifically for server applications. The chipset is stress tested for ECC memory support, a critical feature for server dependability. The ML110 G5 was specifically designed for and rigorously tested with server applications in demanding server configurations. This testing cycle ensures optimal performance and dependability when deployed as a server. And, the ML110 G5 is packaged in an ergonomic chassis that makes typical server hardware configuration changes simple. By not including expensive graphics or sound cards found in desktop PCs the ML110 G5 is able to offer true server functionality at an equivalent desktop PC price.
      Does the ML110 G5 support an Uninterrupted Power System option?
        Yes, a UPS option has been tested and is available for the ML110 G5. Currently, HP supports the usage of an HP T750 or T1000 UPS for the ML110 G5.
      How do the memory offering on the ML110 G5 differ from ML110 G4?
        The memory offering on the ML110 G5 server is DDR2 PC6400 SDRAM (8GB maximum / 512MB standard), unbuffered ECC memory. This new memory runs at a higher speed, which can result in better server performance.

## Slide 16: Full notes page
  To view student notes, go to file menu, choose View, Notes Page
Notes: <header>
<date/time>
Product questions and answers (con’t)
      Why do I need four memory slots?
        Having four memory slots most likely enables systems to accommodate more total memory than a two or three slot solution. Additionally, having up to three open slots allows users to add memory incrementally, growing only as fast as it is necessary. Most importantly for cost-sensitive small businesses, having four slots accommodates large memory configurations without using extremely expensive high density DIMMs. For example, loading 2GB in two slots costs US$3,000-$4,000, more than loading 2GB in four lots (2x1GB DIMMs compared to 4x512MB DIMMs).
      How does USB booting compare to floppy?
        USB 2.0 offers a fast interface for low speed peripheral devices, including storage devices. USB drive keys support large data capacities. Available capacities on USB disk keys can support anywhere from 16 to 300 times more capacity than a 1.44MB floppy disk. ML110 G5 comes without floppy, but offers either USB drive key options in 512MB or 1GB, as well as an external USB Floppy disk drive kit.
      What is PCI-Express and why is it important?
        PCI-Express is the latest serial transmission interface for I/O slots. With transmission rate requirements rising and interfaces moving towards serial, PCI slot is no exception. Within the transition period, HP is keeping two legacy PCI 32-bit slots and offering the new PCI Express slot in the newest ML110 G5 to provide customers the flexibility of different types of existing on hand options, or any new option cards that may need to be implemented. By offering the x4 and x16 form factor PCI Express slot on ML110 G5, SMB customers now have the flexibility in choosing the most suitable I/O options.
      PCI-X slot is not available with ML110 G5, what do I do with options with PCI-X interface?
        The embedded 32bit/33MHz 3.3V PCI slots is capable of utilizing qualified PCI-X controllers.
      Does the ML110 G5 support hot-plug hard disk drives?
        No, the ML110 G5 does not support hot-plug hard disk drives, but adds two hard disk drive bays over the previous generation. Utilizing a non hot-plug solution helps HP to offer the highest value solution to SMB customers. If a hot-plug hard disk drive is desired, customers should consider the ML310 G5.
      Does the ML110 G5 support Serial Attached SCSI (SAS) hard drives?
        Yes. The ML110 G5 supports SAS hard drives in a non-hot plug configuration with the installation of an optional HP 8 Internal Port SAS HBA with RAID (part number 347786-B21).
      Does the HP ProLiant ML110 G5 support embedded SATA RAID in a Windows configuration?
        Yes. However, it requires the use of an optional USB floppy drive (part number DC361B).

## Slide 17: Resources

## Slide 18: Tools and resources
For more information, go to the ML110 G5 home page on HP.com:
  http://h10010.www1.hp.com/wwpc/us/en/sm/WF05a/15351-15351-241434-241646-3328424-3577708.html
Server buying guide
  http://www.hp.com/cgi-bin/sbso/buyguides/tsg_product_select.cgi
ProLiant options
  http://h18004.www1.hp.com/products/servers/platforms/options.html
ProLiant storage
  http://h18004.www1.hp.com/products/servers/platforms/storage.html
Notes: <header>
<date/time>
Tools and resources
    This slide includes helpful tools and resources available on the HP website.

## Slide 19: Regional product marketing contacts
Sales issues |  |  | Presales support issues | 
Product availability Special pricing Qualifying customers Order entry, configuration, or status issues |  |  | Technology or supported configuration questions Planning and deployment scenarios Infrastructure requirements | 
Region | Contact | Email |  | Location
US | Andy Bauman | Andy.bauman@hp.com |  | Houston, TX USA
EMEA | Yan Fei Yang | Yan-fei.yang@hp.com |  | Meyrin, Switzerland
Asia Pacific | Kwang Leng Seah | Kwang-leng.seah@hp.com |  | Singapore
Japan | Iekazu Okano | Iekazu.okano@hp.com |  | Tokyo, Japan
Notes: <header>
<date/time>
Regional product marketing contacts
    For any of the issues listed above, contact the product manager listed for your region.

## Slide 20: Learning check
Notes: Learning check
    1. What are the two main new features of this announcement?
    …………………………………………………………………………………………………
    …………………………………………………………………………………………………
    …………………………………………………………………………………………………
    2. The ML110 G5 is a ………………………………… processor server.
    3. The ML110 G5 server targets which types of customers?
    …………………………………………………………………………………………………
    4. Why should customers buy an ML110 G5 instead using a desktop PC as a server?
    …………………………………………………………………………………………………
    5. What is the HP Lights-Out 100 Remote Management Card?
    …………………………………………………………………………………………………
    6. Your customer requires low-cost servers for an HPC application. What two strengths make the ProLiant 100 series a better choice than the competition? ?
    …………………………………………………………………………………………………
    7. Name three customer opportunities for the ML110 G5.
    …………………………………………………………………………………………………
    …………………………………………………………………………………………………
    …………………………………………………………………………………………………

## Slide 21
Notes: <header>
<date/time>