## Slide 1: HP ProLiant DL160 Generation 5
1. What is new The DL160 G5 server is an Intel-based, 1U form factor, rack-mount server with up to two Intel Xeon™ 5400 sequence quad-core processors. On 14 January 2008, HP will announce the ProLiant DL160 G5 server as follows: Processor refresh — Up to two (2) Intel Xeon™ 5400 sequence quad-core processors running at up to 3.16GHz with 12MB Level 2 Cache. 2. At-a-glance Available processors — Intel Xeon™ 5400 sequence quad-core processors. Model 5472 3.0GHz – 1600MHz FSB Model 5460 3.16GHz – 1333MHz FSB Model 5450 3.0GHz – 1333MHz FSB Model 5430 3.66GHz – 1333MHz FSB Model 5405 2.0GHz – 1333MHz FSB Processor capacity — 2P Form factor — 1U, rack-optimized Memory type, protection, and capacity — PC2-5300 DDR2, Advanced ECC, 32GB maximum memory I/O — Two available PCI Express Generation 2 slots (non-hot-plug models), One available PCI-Express slot (hot-plug models). Storage type — Non-hot plug Serial ATA and hot-plug SCSI/SATA depending on model. Storage controller — HP embedded SATA RAID controller (non-hot-plug models), SC40Ge storage controller (hot-plug models). Remote management — HP Lights-Out 100i High availability — No redundant power supply nor redundant fans Warranty — 1-1-1 | 3. Customer opportunities Look for customers with the following business challenges: High Performance Computing environments. Why? The DL160 G5 is a low cost, 2P Intel Xeon Quad-Core server in a 1U rack form factor. The DL160 G5 has pre-configured, factory-integrated, and tested cluster solutions ideal for High Performance Cluster environments. Customer benefits: Maximum server performance and deployment flexibility with Intel Xeon 64-bit Dual-Core and Quad-Core processor technology, PC2-5300 DDR2 and PCI-Express x16, scale out performance, ultra-dense 2P, 1U form factor for large-clustered or High Performance Computing environments. Reliability and Efficiency. Why? The DL160 G5 supports hot-plug and non-hot-plug hard drives for maintaining data availability and redundancy. Support for Quad-Core Intel Xeon 5400 sequence processors delivering maximum performance with efficient power consumption. Ultra dense 1U rack design offers maximum utilization of server rack and data center space. Customer benefits: An ultra dense 1U rack server providing 24/7 availability and powerful processing power while maintaining an energy efficient total cost of ownership. | Space-constrained corporate datacenters and sophisticated SMBs. Why? ProLiant Lights Out 100i Remote Management and support for IPMI 2.0 industry specifications make server management simple without any added system cost. Corporate datacenters benefit from the 1U form factor, Opteron and I/O performance, and management features. Customer benefits: 1U form factor, rack-optimization, remote management capabilities, flexible deployment options, high performance.. Cost-conscious, sophisticated small and medium businesses. Why? Performance, highly affordable with room to grow by adding processors, memory, hard drives and I/O cards. Internal configuration flexibility supports a variety of applications, and SCSI and SATA models expand deployment options. Customer benefits: Affordable performance-based server, flexible deployment options, investment protection, and new technologies provide a competitive edge. 4. Qualifying the customer Green light deals (must win) The customer: Needs a reliable, and efficient server for general computing. Yellow light deals (more qualification) The customer: Needs high performance computing Wants to create many customized reports Red light deals (walk away) The customer: Is manually troubleshooting application performance problems and does not feel their business or infrastructure is adversely impacted by their process 5. Further information/resources For QuickSpecs, white papers, and technical documentation, go to DL160 G5 on HP.com http://www.hp.com/servers/proliant
© 2007 Hewlett-Packard Development Company, L.P.
The information contained herein is subject to change without notice.
Quick reference card: HP and channel partner use only

## Slide 2: Competition
 | HP ProLiant DL160 G5 | Dell PowerEdge SC1435
Processors | Up to two quad or dual core Intel Xeon™ processors | Up to two dual core AMD Opteron processors
Form Factor | 1U | 1U
DIMM Slots | 8 | 8
Max Memory | 32GB (4GB DIMMs) | 32GB (4GB DIMMs)
Drive support | Up to 4 drives (hot-plug or non-hot plug) 7.2K RPM SATA (160GB, 250GB, 500GB, 750GB) 15K RPM SAS (36GB, 72GB, 146GB, 300GB) | Up to 2 drives (hot-plug or non-hot plug) 7.2K RPM SATA (80GB, 160GB, 250GB, 500GB, 750GB) 10K RPM SAS (146GB, 300GB, 400GB) 15K RPM SAS (36GB, 73GB, 300GB)
RAID Controllers | RAID 0,1 with SC40Ge, RAID 5 with SA E200, P400, P800 | RAID 0,1 with SAS 5iR, RAID 5 with PERC 5i
Ports | 5 USB 2.0 (2F/1int/2R) | 4 USB 2.0 (2F/2R)
Redundant Power Supply | No redundant power supply, optional HE PSU | No redundant power supply, no HE PSU option
Graphics | Integrated 32MB SRAM video | ATI ES1000 controller with 16MB of SDRAM
PCI slots standard | (1) x16 PCI-E G2 (LP), (1) x16 PCI-E G2 (FL/FH) | 1 PCI-Express G1
PCI Slots optional | (1) 133 MHz PCI-X 64 bit (LP), (1) 133 MHz PCI-X 64-bit (FL/FH) | 133 MHz PCI-X (FL/FH)
NICs | (2) Gigabit | (2) Gigabit
Optical Storage | Optional | Optional
Regional contacts | Americas — Tim Golden, tim.golden@hp.com; Latin America Carlos Cuina, carlos.cuina@hp.com EMEA —Tony Bunn, tony.bunn@hp.com ; AP —Naren Nuggehalli, naren@hp.com ; Japan — Iekazu Okano, iekazu.okano@hp.com | 
Notes: Competition
    HP offers the most comprehensive, density-optimized solutions for rack environments that are adaptable to a wide range of complex, growing multi-server environments.
    HP Overall Advantages
      The DL160 G5 offers up to four hard drives (hot-plug or non-hot plug) as compared to two on the Dell model.
      Optional HE PSU where the Dell does not.
      More PCI expansion options
      HP ships more servers than anyone.
      HP is #1 in total worldwide server revenue.
      HP leads the x86-64 Xeon™ EM64T based server market.
      HP continues to lead and gain in the worldwide Windows market.
      HP maintains the lead in the worldwide Linux market.
      HP leads in worldwide shipments in major operating systems.
      HP offers 65,000 service professionals with unmatched technical expertise in over 160 countries, including 28,000 Microsoft trained specialists, 5,200 Microsoft certified experts, 6,500 Linux experts, 5,000 Consultants on J2EE and .NET, 1,400 Cisco experts, and 3,000 SAP experts.
    Proven superior support over Dell
      Dell’s service programs lack global consistency.
      Dell support offerings are not constant across the Dell server lines – low end and high end products are not always eligible for the same service.
      Dell will provide support on “commodity” products, but does not develop expertise on complex products (such as high end storage arrays). Dell will outsource complex issues.
      Dell’s service competencies are Dell products only.
      Dell lacks support for multi-vendor complex environments.
      Dell can support the Wintel environment only.